## Slide 1
Brain_Oil
Predicting 3-Year Cumulative Oil Production with Uncertainty
Kailasadatta Boggaram | Jayanth Damodaran | Bilal Shihab | Carlos Fabela
The University of Texas at Austin
Energy AI Hackathon 2026

## Slide 2
Executive Summary
• Problem: Predict 3-year cumulative oil production for 12 preproduction wells using well logs with missing data and noisy seismic maps
• Approach: MICE+CART imputation at depth level, 19+ engineered features (RQI, FZI), Ridge Regression with two-stage feature selection
• Findings: Ridge Regression outperformed tree-based models (R²=0.9905 vs ~0.82-0.85) due to lower variance on small datasets (n=71)
• Recommendation: For small subsurface datasets, prioritize regularized linear models over tree ensembles; use Bagging for uncertainty

## Slide 3
Problem Statement
• Predict 3-year cumulative oil production (BBL) for 12 preproduction wells (IDs 72-83)
• Generate point estimates + 100 realizations for uncertainty quantification
• Training data: 71 production wells with ~21 depth measurements each
• Challenges: Missing well log data, noisy seismic-derived sand map, small dataset size

## Slide 4
Data & Preprocessing
• Well log features: AI, SI, Vp, Vs, rho, K, G, phi, perm, GR, facies
• MICE + CART imputation at depth level (Van Buuren 2018, Hallam et al. 2022)
• Aggregation: Mean, std, min, max + best/worst zone features for depth heterogeneity
• Sand map: 3x3 smoothing to reduce deliberate noise (per architect guidance)
• Production history: Calculate 3-year cumulative oil from monthly data

## Slide 5
Feature Engineering (19+ Features)
• RQI = 0.0314 × √(k/φ) - Reservoir Quality Index (Amaefule et al. 1993)
• FZI = RQI / (φ/(1-φ)) - Flow Zone Indicator for hydraulic units
• Vp/Vs ratio - Rock physics lithology and fluid indicator
• Best zone features: phi, perm, GR at depth with highest rock quality
• Analog similarity: Distance to top 25% producers in rock quality space
• Spatial proximity: Distance to high-production region centroid

## Slide 6
Feature Selection (Two-Stage)
• Stage 1: Correlation filter removes redundant features (r ≥ 0.98)
• Result: 105 → 61 features (removed 44 highly correlated)
• Stage 2: Stepwise forward selection with 5-fold CV (Miller 2002)
• Result: 61 → 10 optimal features
• Key insight: Dimensionality reduction improves generalization (Guyon & Elisseeff 2003)

## Slide 7
Model Benchmarking Results
Ridge Regression significantly outperformed tree-based models
Model | Test R² | RMSE | Overfitting Gap
Ridge Regression | 0.9905 | 1.57M BBL | 0.002
Random Forest | ~0.85 | 5.2M BBL | 0.15
XGBoost | ~0.82 | 5.8M BBL | 0.18
Linear Regression | Overfit | - | >1.0

## Slide 8
Why Ridge Regression Won
• Small dataset (n=71): Regularization prevents overfitting (Hastie et al. 2009)
• High-dimensional features: L2 penalty handles multicollinearity (Hoerl & Kennard 1970)
• Stability: CV R² std of only ±0.0456 indicates robust performance
• Simplicity: Linear model is more interpretable than tree ensembles
• Key lesson: 'For small datasets, simpler models often win' - Dr. Pyrcz

## Slide 9
Uncertainty Quantification
• Method: Bagging Ensemble with 100 Ridge estimators (Breiman 1996)
• Each estimator trained on bootstrap sample of training data
• Each estimator's prediction → one realization (R_1 to R_100)
• Captures model uncertainty, not just residual noise
• OOB R² validates ensemble quality without holdout data

## Slide 10
Final Model Performance
Model achieves excellent accuracy with robust cross-validation
Metric | Value | Industry Benchmark
Test R² | 0.9905 | Excellent (≥0.93)
CV R² Mean | 0.9539 ± 0.0456 | Excellent
Test RMSE | 1.57M BBL | 4.7% of mean (Excellent <10%)
Features Used | 10 | Optimal via stepwise selection

## Slide 11
Key Innovations
• MICE imputation at depth level (before aggregation) - preserves correlations
• Two-stage feature selection: correlation filter + stepwise forward
• Best zone features capture depth heterogeneity that averages miss
• Systematic benchmarking: 57+ configurations tested to find optimal
• Bagging over residual bootstrap for uncertainty - captures model uncertainty

## Slide 12
Key References
• Amaefule et al. (1993) - RQI/FZI for reservoir quality, SPE
• Breiman (1996) - Bagging predictors, Machine Learning
• Hastie, Tibshirani & Friedman (2009) - Elements of Statistical Learning
• Hoerl & Kennard (1970) - Ridge Regression, Technometrics
• Miller (2002) - Subset Selection in Regression, Chapman & Hall
• Van Buuren (2018) - Flexible Imputation of Missing Data, CRC Press

## Slide 13
Conclusions
• Ridge Regression with stepwise selection achieved R²=0.9905 on test data
• Regularized linear models outperform tree ensembles on small datasets
• MICE imputation at depth level is critical for preserving correlations
• Feature engineering (RQI, FZI, best zone) captures reservoir quality
• Bagging provides robust uncertainty quantification (100 realizations)

## Slide 14
Thank You!
• Questions?
•
• Team Brain_Oil
• The University of Texas at Austin
• Energy AI Hackathon 2026